CRANIAL ORTHOSIS WEARING INSTRUCTIONS

Blanching/redness of the skin is normal

Any blisters or sore spots, discontinue wear of the orthosis and call your orthotist for an appointment to modify the helmet

Wear Schedule:

Day 1:	1 hour on, 1 hour off – three times a day

Day 2:	2 hours on, 1 hour off – three times a day

Day 3: 	4 hours on, 1 hour off – three times a day

Day 4:	6 hours on, 1 hour off – two times a day

Day 5:	6-8 hours on, 1 hour off – two times a day – NO NIGHTS

Day 6:	8 hours on, 1 hour off – two times a day – NO NIGHTS

Day 7:	FOLLOW-UP APPOINTMENT

Wear 23 hours a day once seen at follow-up appointment and fit is 			checked

Hygiene:

Clean the orthosis daily with baby soap and rinse thoroughly, or with rubbing alcohol and air dry.

When possible, air dry the helmet in the sun to help kill bacteria

DO NOT use bleach or any other soaps to clean the helmet

Plagiocephaly Support Site:

http://www.plagiocephaly.org

Your infant has been fit with a Cranial Remolding Orthosis.  This orthopedic device is used to help reduce the effects of deformational plagiocephaly or Brachycehaly.  The Cranial Remolding Orthosis will NOT fit intimately.  By design, there are areas of total contact and relief areas strategically planned into the orthosis.  This encourages more symmetrical and/or proportional skull growth during the treatment program.  A few important points to remember:

- Understand the goals of the treatment program – ask questions if there s any part that is unclear to you!

- Follow the instructions provided for day 1-7.  The introduction period to the orthosis will minimize any discomfort and maximize ease of wear and acceptance of the orthosis.

- Carefully evaluate your infant’s skin each time the orthosis is removed.

- Report any areas of lasting redness or skin irritation to your orthotist immediately.

Wearing Instructions:

- The orthosis may seem a bit ‘loose’ at initial fitting.

- Blanching or pink areas are normal over the areas that growth is being constrained or limited.

- Excessive perspiration during the initial wearing period is normal.

Take special care to clean the orthosis during this time.  It may 	require 2 or more cleanings per day.

Excessive perspiration should taper off by the end of weeks 2 or 3.

- If you observe any sort of skin irritation, discontinue use of the orthosis and contact your orthotist immediately for a follow-up appointment

- Follow the wearning schedule provided by your orthotist.  The schedule below is general and may be modified by your orthotist relative to the needs of your infant.

- Clean the orthosis each day as instructed by your orthotist.

- If there is any concern regarding the fit or function of the orthosis – remove the orthosis and contact your orthotist.

Cleaning Instructions:

Keeping the Cranial Remolding Orthosis clean is as important as any other part of this orthotic treatment program. Daily cleaning will help to prevent potential skin irritation, gives your infant a chance to play without the orthosis and gives you a chance to snuggle his/her little head!

The Cranial Remolding Orthosis must be cleaned at least once per day, however, may require more frequent cleaning during the first 2-3 weeks or wear.  Other factors that would encourage more frequent cleaning are:

a warm climate

increased daily activity levels

outside play

or even just an infant that seems to perspire a bit more than others

Try arranging for an earlier bath time.  This allows a much needed shampooing of the head and the opportunity to really focus on cleaning the orthosis.  Make sure to rinse well and then towel dry the inner surface.  Allowing the orthosis to continue to air dry for the next hour ensures that both the orthosis and your infant’s head are completely dry before reapplying.

HELPFUL HINTS:

Shampoo and/or rinse your baby’s hair each day at bath time.

Clean the orthosis each day with a slightly diluted rubbing alcohol (78-99%).

Rinse well……and then rinse again!

Wipe dry with a towel, or place the orthosis in front of a sunny window, if possible.

A hair dryer set on ‘COOL’ may be used to speed the drying process.

Allow the orthosis and your baby’s head to dry completely before reapplying.

NEVER, EVER use harsh household cleaners.